## Slide 1: Determination of 14C abundance in liquid scintillator
V. Sinev
INR RAS, Moscow Russia
In collaboration with
I. R. Barabanov, L. B. Bezrukov, A. V. Veresnikova, V. Yu. Grishina, V. I. Gurentsov, V. P. Zavarzina, S. D. Krokhaleva, A. S. Kurlovich, B. K. Lubsandorzhiev, S. B. Lubsandorzhiev, A. K. Mezhokh, G. Ya. Novikova, A. Yu. Sidorenkov, V. V. Sinev, E. A. Yanovich,
Yu. M. Gavrilyuk, A. M. Gangapshev, V. V. Kazalov, V. V. Kuz’minov, V. B. Petkov, A. M. Pshukov, Sh. I. Umerov
V. P. Morgalyuk
P. Yu. Naumov,
T. Enquist, P. Kuusiniemi, J. Joutsenvaara, A. Virkajarvi
INR RAS, Moscow
BNO INR RAS, Baksan
INEOS, Moscow,
MEPI, Moscow
Univ. Oulu, Finland
50-th Anniversary of Baksan Neutrino Observatory, Nalchik, June 6-8 2017

## Slide 2: Plan
Introduction
Detector for liquid scintillator tests
Detector backgrounds
LAB measurements
Conclusion

## Slide 3: Introduction
For large scintillation detectors the key problem is threshold, which is limited by the 14C contamination.
We decided to check the hypothesis that in coal solvent the abundance of 14C is less than in oil one.
For this purpose we have organized at Baksan NO the laboratory to measure samples of liquid scintillator to determine 14C abundance.

## Slide 4: Borexino detector and 14C
Fiducial mass 100 t ,
Total 300 t

## Slide 5: Borexino measured spectrum of recoil electrons

## Slide 6: Recoil electrons spectrum from 40K in BOREXINO

## Slide 7: Setup for measuring abundance of 40K in small samples of liquid scintillator

## Slide 8: Detector
Light guide
Photo multiplier
The cuvette filled with explored liquid

## Slide 10: Scintillator on base of linear alkyl benzene (LAB)
LAB is a mixture of hydro carbonates with a formula like CnH2n-6. Density is between 0.855 and 0.858 g/cm3. Flash point is 143°C.
In our sample we have 4 fractions: C16H26(12.5%), C17H28(29.3%), C18H30(31.5%), C19H32(26.7%).
Light yield is about 8000 photons per MeV
Attenuation length at 420 nm 15 m.

## Slide 11: Used electronics
S
Digital oscilloscope NI5015
A
Trigger
PMT 1
PMT 2

## Slide 12: Backgrounds
Uranium and thorium chains are not in equilibrium in cooper shielding and scintillator itself.
We regard the rest of uranium and thorium after purification and amount of their products after several years passed after purification.
Radon can penetrate in shielding gaps and in the scintillator volume.
Potassium-40 comes mainly from voltage dividers.
Cerenkov light emitting in light guides due to energetic gammas from shielding.

## Slide 13: Backgound parts
238U inside
238U outside
232Th inside
232Th outside
222Rn inside
222Rn outside
Cerenkov light
40K outside

## Slide 14: Comparing of spectra from scintillator and from light guides and pmt glass.

## Slide 15: Calibration

## Slide 16: 14C LAB sample measuring with 222Rn

## Slide 17: 14C LAB sample measuring with 222Rn decayed

## Slide 18: Conclusion
Low background setup placed at Baksan underground laboratory is available to start researches of scintillator samples
First measurements show backgrounds should be better depressed to see clearly 14C spectrum.
To the moment we began to understand the origin of backgrounds in our detector and started to simulate these backgrounds.
Measured 14C/12C ratio for the LAB (Russia, 2017) sample is (3.2 ± 1.1) × 10-16 and (5.5 ± 1.0) × 10-16 for LAB (China, 2017).